CPRA /CPIN NEWSLETTER FOR MAY 2018

The next CPRA/CPIN meeting will be held Thursday, April May 17, 2018 at Hoss’s in Hummelstown at 7 PM.  Come at 6 PM for food and beverage.

Dan Rapak, WA3ATV, restored microwave service at Eagles Peak.  This site is half-way between Cornwall Mountain and Mount Penn in Reading.  Eagles Peak and Reading receive signaling data from the railroad and send it to WA3ATV.  The BARC group in Reading uses the internet to connect their repeaters to the outside world. The reason for the failure was a bad CAT5 connector. The link to Ephrata mountain was not working either.  The Rocket M5 transmitter was replaced and the circuit was restored.

The CPIN network was out of service twice on Wednesday, May 9, 2018.  The first outage occurred at 3:30 AM to 7:15 AM. Comcast was doing maintenance at 3:30 AM and caused the modems to reboot through out the Comcast network.  The router that connects CPIN to the Comcast network uses DHCP and lost its connection to the modem.  The router was rebooted and service was restored.  One possible solution to prevent this from happening in the future would be to use a static IP address in the router rather than using DHCP.

The second outage occurred several hours later. A gigabit switch was removed from service.  A Cisco 2950 switch was placed between the router and the Ubiquity transmitter.  Sometimes a trunk port will display VLAN 1 and then change to trunk.  In this case it didn’t change.  It only passed VLAN 1 and LAN traffic.   All the other VLANs were blocked.  Service was restored by using a port that displayed “trunk”.  The failed port was reprogrammed as a trunk.  But it still displayed VLAN 1.  Further testing is needed.

The several of the older Rocket M5s were upgraded to the latest firmware.  The spectrum analyzer did not need JAVA any longer.  And it started within a few seconds.  But the radio  was missing the following bands: 5.15 to 5.25, 5.25 to 5.35, and 5.47 to 5.725.   The help desk at Ubiquity advised: no problem just follow these instruction:

- Request lower band activation key and labels from Ubiquity

- Down grade the radio to v5.5.11 to get the option to enter UNii key

- Version 6.1.6 is a signed firmware so to downgrade you will need to load up v6.0.6beta then 5.6.15, then 5.5.11

- Then load 6.1.6

DMR Update

WAG GAP: UHF DMR radio to be ordered directly by South Middleton TWP.

Lancaster City DMR radio waiting for successful grant from pipeline.  Other sources may be

Available if grant is not awarded.

Ten channels of video are currently available on the CPIN network.

1. Waggoner's Gap: three cameras

2. Reeser's Summit: one camera inside shelter

3. Blue Mtn at WITF/WHP: three cameras: two outside and one inside

4. Cornwall Mtn: three cameras at the Ranger Station

These cameras are viewable 24/7

Go to:  173.163.115.137:7080

username: cpin         password:  cpin

Tell us where you want to see cameras added.  Four more cameras are ready to be installed.

MPEG4 is used by all cameras.  Some are SD and some are HD

MOTUS personnel came back this month to WAG GAP.  The flight data from the migrating birds was down loaded from an SD card. Their equipment indicated 46 momentary power interruptions.  The power company will need to investigate this further. The non-commercial FM radio station at the site was notified.

Anytone 868UV CPS Programing: FM Radio

FM radio stations can be programmed into the Anytone handheld.  The logical choice would be FM radio stations that broadcast on the Emergency Alert System (EAS).  The PEMA web site has a link to the current EAS State Plan.

http://www.pema.pa.gov/planningandpreparedness/Documents/Complete%20PA%20EAS%20Plan.pdf

The Emergency Broadcast System (EBS), occasionally called the Emergency Broadcasting System and sometimes called the Emergency Action Notification System (EANS), is a former emergency warning system used in the United States. It replaced the previous CONELRAD system and was used from 1963 to 1997, at which point it was replaced by the Emergency Alert System.

All eight of the FM radio stations in the next paragraph have been entered into the Anytone Handheld code plug effective 3/23/18.  To activate reception, go to menu, scroll down to settings, then select radio settings, scroll down to #27 FM radio, scroll down to Radio On and select it.  This will activate the FM radio continuously. Turn the channel selection knob for the FM radio station of your choice.  Only eight stations are in the memory. The handheld will only function as an FM radio receiver at this point and will not receive VHF or UHF signals.  To add VHF and UHF signals as a priority, go to #28 FM Radio Monitor, scroll down to FM Monitor On and select it.  You are now listening to the selected FM radio station but will still hear the VHF and UHF signals as a priority.

South Central Pa has four regions:

CAPITAL: Cumberland, Dauphin, Lebanon, Perry Counties

Local Primary Station #1: WRVV-FM 97.3   Local Primary Station #2: WITF-FM 89.5

CHAMBERSBURG: Franklin, Fulton Counties

Local Primary Station #1: WPPT-FM 92.1   Local Primary Station #2: WIKZ-FM 95.1

LANCASTER: Lancaster County

Local Primary Station #1: WROZ-FM: 101.3   Local Primary Station #2: WLAN-FM 96.9

YORK: Adams, York Counties

Local Primary Station #1: WARM-FM 103.3   Local Primary Station #2: WGTY-FM 107.7

If you have changes to the AT-868UV code plug that would benefit users in SCPA, then request those changes to: WA3CPO@ARRL.NET .

CODE PLUG for ANYTONE D868UV   Dual band handheld

Go to: www.w3nd.org   under system

NETWATCH

- Control Center Interstate Network (our current C-Bridge for SCPA, in transition)

http://cbridge.wr3irs.com:2135/MinimalNetwatch

- Control Center K4USD Network (Our former C-Bridge)

http://cbridge.k4usd.org:42420/MinimalNetwatch

- Brandmeister Network

https://brandmeister.network/?page=lh

- Control Center DCI

http://www.trbo.org/cBridge/netwatch.html

DEEP CYCLE BATTERIES

The availability has been verified. They will be available in twelve months.

The currently available batteries will be used with the DMR repeaters to avoid momentary interruptions of power.  So far it has been a success.

BRANDMEISTER SPEAKER

A nation wide Brandmeister speaker may be available in the fall

Dues: are $20/yr for a single membership and $35/yr for a family membership, which includes all licensed amateurs living in one household.  If you have not renewed please do so…we need your support!  If you have, consider an additional donation!  Renewal is due in April.

# use the revised membership application shown BELOW

Thanks!   Please make your check payable to:

# Central Pennsylvania Repeater Association, Inc.

# C/O Terry Ash

4335 Rodkey Road, Harrisburg, PA  17110

# DO NOT SEND CASH!

# APPLICATION FOR MEMBERSHIP IN CPRA

□ 2016    □ 2017   □ 2018   □ 2019

□ New member    □ Renewal   □ Family   □ Updating Information

□ Donation ______________     □ Other ______________________

# Dues are $ 20.00 Individual and $ 35.00 Family.

# Total amount enclosed $ ____________

Name:___________________________________   Call(s)_________________

# Address: ______________________________ City: ______________________

# State: ________  Zip code __________  License class: ____________________

Email address for newsletters: ________________________________________

Phone: _______________________  	   □ Listed               □ Unlisted

Are you an ARRL member?   □ Yes         □ No

Are you a member of WITF    □ Yes         □ No

# EMERGENCY RACES VOLUNTEER INFORMATION

This information will only be used in the event of an emergency.  This information will only be given to the emergency RACES coordinator and will not be distributed for general information in any form!

# Work number including extension:  _______________________________

# Cell Phone:  _________________________________________________

Email address:  ______________________________________________